## Slide 1: LOGISWARM
Logistics Using Semi-Automated Multi-Robot Systems

## Slide 2: Flow of Presentation
Problem Statement
Abstract
Objectives of the Project
Applications
State of the art
BudgeBOTS
Pushing strategies
LOGISWARM-Testbed
Flowchart – Working
Implementation
Impact
Budget
Outcomes
Projects completed
Achievements

## Slide 3: Problem Statement
Automated Guided Vehicles (AGVs) – conventional means of payload relocation within a warehouse
AGVs – highly static system
Payload – different shapes and sizes
Light payload movement with AGVs is inefficient
AGVs – cannot carry payloads of larger size than it’s capacity
Technology breakdown interrupts functioning of whole system
Human interference causes undesired error
Unnecessary cost involved with human labour

## Slide 4: Abstract
Multi Robot System - A system consisting of multiple robots which can cooperate and communicate with each other to accomplish certain tasks
LOGISWARM simplifies the process of transporting payload within a warehouse by cooperative transport using Multi-Robot Systems
Our goal is to help manage problems in a warehouse such as
  Inventory
  Cost
  Time
  Prevention of technology breakdown

## Slide 5: Objectives of LOGISWARM
The follower robots will take the leader’s direction as the input and generate the summed output force that aligns in the same direction as the input and has larger magnitude than the input force
The most efficient way of payload movement will be determined by analysis of various object pushing strategies

## Slide 6: Applications
Warehouse logistics
Airports and Railway stations.
Extended applications
  Underwater Search and Rescue
  Plastic Removal from River Banks
  Simultaneous localization and mapping (SLAM)

## Slide 7: State of the art
The act of collective transport can be broken down into two phases.
  The first phase involves BudgeBOTs being placed around the object to grip it.
  The second phase involves the agents applying forces to the object to transport it to the goal.
Two or three implementations are introduced and analyzed, accounting for two different classes of object dynamics:
  small objects where kinetic friction dominates
  and large objects where inertia dominates.
(7)

## Slide 8: BudgeBOTS
ATMEGA based differential drive robots – Two wheels for locomotion and two castor wheels for support
3D printed body
Radio Frequency Communication
3.7 V Lithium rechargeable Polymer Battery
Can collectively transport complex shaped and irregular payloads
Approx run-time (on battery) is 40 mins

## Slide 9: Pushing strategies
Number of robots employed according to shape and size of payload
Object closure strategy implemented
Pushing strategy helps transport payload to the goal
Limitations -
  Size of object should be lesser than the testbed
  Friction

## Slide 10: LOGISWARM-Testbed
The LOGISWARM – testbed will be used for testing of our robots
Dimensions – 100cm*60cm
Overhead camera (Logitech C270 HD Webcam) – for tracking AprilTags / Fiducial markers
The testbed will also have charging stations for robots

## Slide 11: Flowchart - Working
CONSENSUS THEOREM STATES THAT A ROBOT TENDS TO GET THE AVERAGE OF THE STATES OF IT’S NEIGHBOURING ROBOTS AND EVERY ROBOT SHARES A COMMON STATE AFTER A CERTAIN TIME.
(11)

## Slide 12: Implementation
  Various stages called WORK-PACKAGES (WPs)
  Deliverable will be obtained after completion of each work package
  Each work package will be assigned to the respective domain
  Everything will be compiled for completion of LOGISWARM
  Improvements will be done through evaluation, testing, research and development

## Slide 13: WORK PACKAGE 1
Testbed:
Platform for testing of robots
Feedback system for detecting position and orientation of robots
using an overhead camera ( Logitech C270)
Charging station for robots
Dimensions of testbed : 100cms*60cms
DELIVERABLE (D1) – Testbed with Overhead Camera

## Slide 14: WORK PACKAGE 2
Single Robot Prototype
Specifications:
  ATmega based differential drive robot
  3D printed body
  RF communication
DELIVERABLE (D2) – Working single robot
  prototype

## Slide 15: WORK PACKAGE 3
Teleoperated Robot
Single BudgeBOT can be taken to goal location using remote control
  Remote Controller will be fabricated
  Communication using Radio Frequency
  Feedback using Overhead Camera
  Range of remote controller is 50metres
  DELIVERABLE (D3) – A leader robot with remote controller

## Slide 16: WORK PACKAGE 4
Directional consensus Multi-robot system
  Initially ,robots will be randomly oriented
  Instructions will be sent to leader robot only
  After sometime follower robots will achieve same state according
  to directional consensus
  DELIVERABLE (D4) – Multi-Robot System capable of co-ordination

## Slide 17: WORK PACKAGE 5
LOGISWARM completed for testing and evaluation
  Robots will cage the object and transport object to desired location
  Followers amplify leader’s force to achieve the task
  DELIVERABLE (D5) – LOGISWARM completed for testing and evaluation
(17)

## Slide 18: Timeline
The deadline for the deliverables have been summarized in the following Gantt Chart :
 | M1 | M2 | M3 | M4 | M5 | M6 | M7 | M8 | M9 | M10 | M11 | M12 | M13 | M14 | M15
WP1 |  |  | D1 |  |  |  |  |  |  |  |  |  |  |  | 
WP2 |  |  |  |  |  | D2 |  |  |  |  |  |  |  |  | 
WP3 |  |  |  |  |  |  |  |  | D3 |  |  |  |  |  | 
WP4 |  |  |  |  |  |  |  |  |  |  |  | D4 |  |  | 
WP5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D5

## Slide 19: Impact
BudgeBOTs will be tested for different scenarios and efficiency in different scenarios will be analyzed and improved
Initially, BudgeBOTs will have a leader robot which will be remotely controlled, and the follower robots will be autonomously sync with the leader robot and its nearest neighbors. Further development can be done to make the system fully autonomous which will make human interruption almost null
employment of BudgeBOTs will also reduce the amount of human intrusion thereby minimizing errors occurring due to human fatigue

## Slide 20: Budget for a single BudgeBOT
S.No. | PARTS | Cost/piece | QUANTITY | COST (IN ₹)
1. | PCB | 350 | 1 | 350
2. | Lithium Polymer Battery | 700 | 1 | 700
3. | RF Module | 400 | 1 | 400
4. | Motor drivers | 350 | 1 | 350
5. | SMD Passive Components |  | 20 Resistors & 15 Capacitors | 300
6. | 3V-6V DC Motors | 200 | 2 | 400
7. | NRF24L01+ | 350 | 1 | 350
8. | Microcontroller | 300 | 1 | 300
9. | Castor wheels | 10 | 2 | 20
10. | Voltage Regulator | 200 | 1 | 200
11. | IR sensors | 31.25 | 8 | 250
12. | Switches | 75 | 6 | 450
Total |  |  | ₹4070 * 1.5 = ₹6150 | 
Price Estimate of 30 Robots @ ₹6150 each is ₹1,84,000

## Slide 21: Budget (contd.)
S.No. | DESCRIPTION | Cost/piece | QUANTITY | COST in ₹
1. | 3D Printing Filament | 30,000 |  | 30,000
2. | Soldering Station | 3,500 | 2 | 7,000
3. | Hot-Air Station | 4,500 | 2 | 9,000
4. | Soldering Tools – Lead, Flux, Solder Paste, Wire Cutter, Tweezers, Solder Sucker, Solder Wick |  |  | 20,000
5. | Connectors – Jumpers and Headers |  |  | 6000
6. | Testing Boards – Breadboards and Perforated Boards |  |  | 7000
6. | Multimeter | 600 | 2 | 1200
7. | Testbed and Overhead Camera | 18,000 | 1 | 18,000
8. | Atmel ICE Programmer | 15,000 | 1 | 15,000
9. | Conferences and Competition Participation |  |  | 45,000
10. | Miscellaneous |  |  | 10,000
TOTAL |  |  | ₹1,68,200 | 

## Slide 22: Budget (contd.)
Price Estimate for 30 BudgeBOTs = ₹1,84,000
Price Estimate for Consumables and Electronic Equipment = ₹ 1,68,200
TOTAL BUDGET = ₹3,52,200

## Slide 23
PATENTS
A patent on multi robot testbed for research
CONFERENCES
IROS-International Conference on Intelligent Robots and Systems
ICRA-International Conference on Robotics and Automation
ROBIO-International Conference on Robotics and Biomimetics
JOURNALS
International Journal of Robotics and Automation (by ACTA press)
Industrial Robot : An International Journal
IEEE Robotics & Automation Magazine
Outcomes

## Slide 24
Projects Completed
Sprinter : A multi-robot printing system
  A multi robot system capable of printing over a surface as they move.
  The entire task of printing is divided among all the sprinters.
  They communicate and coordinate themselves to complete the
  printing.
  Printing can be done irrespective of the paper size.
  Amount Sanctioned ₹80,000
  Amount Spent ₹1,60,000

## Slide 25
Achievements in 2017 Siemens MakeITReal Hackathon 2017 Finalists WSSIMP Workshop Demo | Achievements in 2018 International Autonomous Robotics Competition (IARC) Finalists, Techriti, IIT Kanpur The Institution of Engineers India (IEI) PCB Design, Fabrication and Testing Workshop Organizers IEI Machine Learning for Intelligent Speech (MLSIP) Workshop Demonstration Siemens MakeITReal Hackathon 2018 Finalists Tecknicus (An initiative taken to educate school students the basics of electronics) The Institution of Engineering and Technology (IET’s) IOT India Congress Demo, IOT based mobile printer Publication of the paper ‘Perturbation Analysis in Decentralized Estimators’ in the proceedings of IEEE International Conference on Robotics and Biometrics (ROBIO), Kuala Lumpur by Kedar Prasad Karpe, Dhanalakshmi Samiappan, Kumar Ramamoorthy and Lorenzo Sabattini. | Achievements in 2019 First place in Line Follower competition at Daksh, Sastra, IIT Madras Third place in Line Follower competition at Roboprix, VIT Chennai
Achievements

## Slide 26: THANK YOU